# Sistema  C 70 CORREDERA PVC

Supply and fitting of 16 mm groove windows/doors comprising of PVC profiles that, according to their dimensions and design, ensures the system’s resistance and the ability to keep its shape.

It has a frame depth of 170 mm and 46 mm in the sash.

Categories achieved at test bed*:

Air permeability according to UNE-EN 12207:2000 norm	 	 Class 4

Water tightness according to UNE-EN 12208:2000 norm                Class  5A

Wind resistance according to UNE-EN 12210:2000 norm                Class  C5

* Test reference on a window measuring 1.20 x 1.20 mts. 2 sashes

Surface finish:

Surface of (colour …………, imitation timber ……….) achieved by way of a lamination on the base profile with a high resistance solar radiation thermo welded film that has been tested on an accelerated ageing test bed.