# System  4500 ELEVATING SLIDER with THERMAL BREAK

Supply and fitting of Cortizo Groove sliding windows and doors comprising of 6063 aluminium alloy profiles with T5 thermal treatment along with exclusive Cortizo Groove hardware and accessories in order to guarantee that it operates well and to guarantee the results obtained in the tests.

The frame and sash have a sectional area of 100/123/127/185 mm & 51 mm respectively and a 25 mm glazing space. The average aluminium profile wall thickness is 2 mm.

The aluminium profiles are designed to be thermally broken which is achieved by inserting polyamide 6.6 isolation strips, 24 mm wide in the frame (elevating version) and 30 mm wide in the frame (in-line version) and 14.6 mm in the sash, that are reinforced with 25% fibre glass.

Hardware

Elevating version:

An elevating and sliding gearing is incorporated that allows for easy sash sliding of large weights over a stainless steel rail that prevents wear of up to 400 kgs. per sash, and dimensions of up to 3.35 mts. in length and 2.90 mts in sash height. In the open position, the elevated sash forces the bearing to work and allows a controlled airing as there is no contact with the frame gasket. In the closed position it offers perfect weather tightness around the total perimeter as the gaskets are compressed by the weight of the sash.

In-line version:

A slider gearing is incorporated that allows for easy sash sliding over a stainless steel rail that prevents wear of  large weights up to 280 kgs. per sash and dimesnions of up to 3.35 mts. in length and 2.90 mts. in sash height.

Classifications achieved at test centre*:

Air permeability according to EN 12207:2000		Class  3

Water tightness according to EN 12208:2000 		Class  8A

Wind resistance according to EN 12210:2000		Class  C4

* Test reference 1,85  x 2,05  m. 1 Sash + 1 Fix.

Surface Finish:

-Powder coating in ..……….   carried out with a complete cycle that includes de-greasing, strip clean in a bath of caustic soda, wash, controlled oxidisation, drying and thermocoated using polyester powder applied electrostatically and a subsequent curing at 200 ° C. The quality of the paint coating is guaranteed by the QUALICOAT seal of approval and the thickness is between 60 & 100 microns.

-Anodized, finish………..  colour............ carried out with a complete cycle that includes de-greasing, wash, anodic oxidation, coloring and sealing operations. The thickness and quality of the anodic coating is guaranteed by EWAA-EURAS seal with a minimum class……... microns.