# System SOLAR PROTECTION LOUVRES

Supply and fitting of profiles for a solar protection system comprising of general modules of …………in dimension and made up of ……….. sight areas using profiles in 6063 alloy with T5 thermal treatment.

A load bearing structure comprising of ………. mullions type COR-9159 with a seen surface of 45 mm which ensures perfect resistance to bending when subject to wind action and excess snow weights, glass and its own weight.

Fixed louvres with various angle possibilities. Adjustable louvres that are motor driven with a range of ………… mm

The louvres are fixed using 5754 laser cut aluminium sheet, between 3 & 6 mm thick,and then painted.

Classifications achieved at test centre*:

Test carried out according to UNE 1932: 2001 norms.

UNE 13659:2004----- Class 6 (MAX)

Surface Finish:

-Powder coating in ..……….   carried out with a complete cycle that includes de-greasing, strip clean in a bath of caustic soda, wash, controlled oxidisation, drying and thermocoated using polyester powder applied electrostatically and a subsequent curing at 200 ° C. The quality of the paint coating is guaranteed by the QUALICOAT seal of approval and the thickness is between 60 & 100 microns.

-Anodized, finish………..  colour............ carried out with a complete cycle that includes de-greasing, wash, anodic oxidation, coloring and sealing operations. The thickness and quality of the anodic coating is guaranteed by EWAA-EURAS seal with a minimum class……... microns.